## Slide 1
2020
Computer Architecture
Subject: Computer Architecture
Text Book:
Computer system Architecture By
M. MORRIS MANO
Lecture 1

## Slide 2
Lecture 1
Computer Architecture
Course Schedule |  |  |  |  |  | 
Week | Topic | Mapping to CLO | Mapping to PLO | Assignment(s) | Quizzes | lectures
1 | Introduction to Computer Architecture | 1 | a |  |  | Lecture 1
2 | Digital Logic Circuits and Components | 2 | a |  |  | Lecture 2
3 | Number Systems, Arithmetic operations | 2 | a |  |  | Lecture 2
4 | Register Transfer Language and Micro- Ops | 3 | c | Assignment 1 CLO 1 |  | Lecture 3
5 | Register Transfer Language and Micro- Ops | 3 | c |  | Quiz 1 CLO 2 | Lecture 3
6 | Basic Computer Architecture and Design | 2, 3 | a,c |  |  | Lecture 4
7 | Basic Computer Architecture and Design | 2, 3 | a, c |  |  | Lecture 4
8 | Midterm Exam |  |  | CLO 1,2,3 |  | 
9 | Computer Arithmetic Unit Design | 2, 3 | a,c |  |  | Lecture 5
10 | Computer Arithmetic Unit Design | 2, 3 | a,c |  |  | Lecture 5
11 | Programming the Basic Computer | 3 | c | Assignment 2 CLO3 |  | Lecture 6
12 | Central Processing Unit CPU Design | 4 | a |  | Quiz 2 CLO4 | Lecture 7
13 | Central Processing Unit CPU Design | 4 | a |  |  | Lecture 7
14 | Pipeline and Vector Processing | 5 | a |  |  | Lecture 8
15 | Multiprocessor Design | 5 | a | Assignment 3 CLO 5 |  | Lecture 9
16 | Revision and problem solving |  |  | CLO 2,3,4,5 |  | Lecture 10
 | Final Exam |  |  |  |  | 

## Slide 3: Lecture : 1 INTRODUCTION TO COMPUTER ARCHITECTURE
Lecture 1
Computer Architecture

## Slide 4: Microprocessors
The Microprocessors is one of the most important technological achievements since the development of the transistor.
It was first introduced into the market place by INTEL Corporation in 1971.
Lecture 1
Computer Architecture
7

## Slide 5: Microprocessors
Lecture 1
Computer Architecture
The Microprocessor is a Central Processing Unit (CPU) that is usually implemented in a single integrated circuit Package.
Microcomputer is consisted with:
  Microprocessor ,
  Memory ,and
  Input\Output (I\O) devices,

## Slide 6: Microcomputers
The Architecture:
Figure 1. Block diagram of a basic Microcomputer
Microprocessor
Input Device
Memory Address Bus
Input Bus
Output Bus
I\O Bus
Memory data Bus
Memory
Output Device
Lecture 1
Computer Organizatio6n

## Slide 7: Microcomputers – Building Blocks
7
Input Devices:
  Convert input signals into the proper binary form for the Microprocessor.
  Typical input devices are:
    Keyboards,
    Teletypewriters,
    Analog-to-Digital converters (A\D),
    Digital-to-Analog converters (D\A)
Lecture 1
Computer Architecture

## Slide 8
Input Devices (continued):
  Requires an interface Network to transform the input data into the compatible digital form.
  Receives data through an Input Bus.
  Selects the input device by sending out an address on the I\O Address Bus.

## Slide 9: 2- Memory:
Has the ability to store binary Numbers that describes in detail the instructions to be executed by microprocessor.
By sending out an address on the memory bus, the microprocessor requests a memory location.

## Slide 10
Memory (continued):
  The memory, either accepts data from the memory data bus into this location
(write operation)
  or
  it sends data from the this location to the microprocessor over the memory data bus
(read operation)

## Slide 11: 3- Microprocessor:
– Contains a CPU that consists of the circuitry required to access the appropriate locations in memory and interpret resulting instructions.

## Slide 12
Microprocessor (continued):
  The CPU consists of:
    Arithmetic\Logic Unit (ALU), that performs arithmetic and logical operations on the data
    Control Section, which controls the operations of the computer.
    Data Registers for temporary storage and manipulation of data and instructions

## Slide 13: 4- Output Devices:
Convert the binary output data into a useful form.
Typical input devices are:
  Printers,
  Cathode Ray Tube (CRT) displays,
  Digital-to-Analog converters (D\A)

## Slide 14
Output Devices (continued):
  Receives data from the microprocessor through an
Output Bus.
  The required device is selects by the microprocessor through the I\O Address Bus.

## Slide 15
In many microcomputer systems, the input and output devices, as well as the memory, share one or more buses, as shown in figure 2.
Data Bus
Address Bus
Figure 2. Microcomputer system sharing data and address buses.
Microprocessor
Memory
Input Device

## Slide 16: Microcomputers – Building Blocks
The Memory Data Bus, the Input Bus and the Output Bus share the single Data Bus.
The Memory Address Bus and the I\O Address Bus are implemented into a Common Address Bus.
Computer Organizati1o9n
Lecture 1

## Slide 17: Microcomputers – Building Blocks
17
Bus: is a group of parallel conductors (wires) which carry information.
I\O Port: is the point at which the I\O device is connected to the microcomputer.
Lecture 1
Computer Architecture

## Slide 18: A Microcomputer: is Capable of performing many different operations.
Lecture 1
Computer Architecture
18
It can add and subtract numbers and
It can perform logical operations.
It can read information from an input and transmit information to an output device.
In fact, depending on the microprocessor used, there may be 100 or more different operations that the microcomputer can perform.
Moreover, two or more individual operations can be combined to perform much more complex operations.

## Slide 19: Microcomputers – Building Blocks
Lecture 1
Computer Architecture
19
An instruction: is the operation that the computer can be told to perform.
For example: ADD, BUBTRACT, LOAD, STORE, HALT, etc.
A program: is a group of instructions that allow the computer to perform a specific job. The length of the program is proportional to the complexity of the task (job) that the computer is to perform.

## Slide 20: Microcomputers – Building Blocks
Lecture 1
Computer Architecture
20
A bit: is a binary digit (0 or 1).
A Byte: is a group of bits that are used as a single unit. It consists of 8 bits
A Word: is a group of binary digits.
  In the 8-bit microprocessor, each word consists of one byte.
  In the 16-bit microprocessor, each word contains two bytes.

## Slide 21: Microcomputers – machine cycle
Lecture 1
Computer Architecture
21
The microcomputer operates in synchronism with a clock. To accomplish the task specified by one instruction, a number of clock cycles are required.
Instruction Cycle:
is the execution of one instruction.
An Instruction consists of one or more machine cycle.

## Slide 22: Microcomputers – machine cycle
Lecture 1
Computer Architecture
22
During a machine cycle, the following
sub-cycles are performed:
Fetch cycle
Execute cycle

## Slide 23: Microcomputers – machine cycle
Lecture 1
Computer Architecture
23
Fetch cycle:
  The CPU provides the address of an instruction through the address bus .
  The address is decoded by the memory, and the instruction is read from the memory into the CPU through the memory data bus.

## Slide 24: Microcomputers – machine cycle
Lecture 1
Computer Architecture
24
Execute cycle:
  The instruction is decoded by the CPU, and the request operation is performed.

## Slide 25: Microcomputers – machine cycle
Instruction read from
Lecture 1
Computer Architecture
25
memory
Instruction executed
Fetch cycle
Address send to memory
Execute cycle
Machine cycle
Typical machine cycle

## Slide 26
Lecture 1
Computer Architecture
26
Memory may be divided into two classes:
  Read- Only memory (ROM) , PROM
,EPROM ,…..
  Read-Write memory (RWM) or (RAM).
Memory System: is divided into three main parts:
  TPA (Transient program area).
  System area.
  Extended memory.

## Slide 27
Memory System: is divided into three main parts:
  TPA (Transient program area):
    Is used to hold the operating system and other programs that control the computer system.
    Also holds any currently active application program.
    The size of TPA is 640 k BYTES.
Lecture 1
Computer Architecture
27

## Slide 28
Memory System: is divided into three main parts ( continue …….:
  System Area:
    Contains programs on a ROM and RAM for data storage.
Lecture 1
Computer Architecture
28

## Slide 29
Lecture 1
Computer Architecture
29
Memory System: is divided into three main parts ( continue …….:
3. Extended Memory:
(15 M Bytes in 80286), (31 M Bytes 80386 SL), ( 4095 M Bytes 80386 DX, 80486)

## Slide 30: Microprocessor
Lecture 1
Computer Architecture
30
It is the controlling element in a computer system.
Some times it is referred to as CPU.
CPU consists of an ALU (Arithmetic and Logic Unit), Approximate Registers, and Control Circuit.

## Slide 31: Microprocessor
Lecture 1
Computer Architecture
31
The steps involved in executing a program consists of transferring binary quantities from one register to another and performing Arithmetic and Logic Operations on these quantities.
A number of important registers are normally included in the CPU.

## Slide 32: Microprocessor
Lecture 1
Computer Architecture
32
They are used for temporary storage of data and
instructions by the machine.
The most common registers included are :
  Memory Address Register (MAR)
  Memory Data Register (MDR)
  Accumulator (AC)
  Program Counter (PC)
  Stack
  Stack Pointer
  General-Purpose Register
  Instruction Register (IR)
  Status Register

## Slide 33: 1. Memory Address Register (MAR):
Lecture 1
The MAR holds the address of the word to be accessed in memory.
The size of the MAR determines the number of words in memory that the microprocessor can directly address.
For Example:
  a 16-bit MAR will address 2 ^16= 65,536 words directly.

## Slide 34: 2. Memory Data Register (MDR):
Lecture 1
The MDR receives and holds a word from
memory through the data bus.
The size of the MDR is determined by the number of bits in a data word.

## Slide 35: 2. Memory Data Register (MDR):
Lecture 1
For Example:
  A one-Byte word size requires an eight-bit
MDR.
  A word being written into memory is also held in this Register until the write operation is complete.
  The MDR may be as a buffer in the microprocessor.

## Slide 36: 3. Accumulator (AC):
Lecture 1
Computer Architecture
36
The result of the Arithmetic and Logical Operations (in the ALU), are stored in the AC.
Also serves as one input to the ALU.

## Slide 37: Register B
ALU
Accumulator
Figure 4. Function of the Accumulator
37
Lecture 1
Computer Architecture

## Slide 38: 3. Accumulator (AC):
For Example:
  Suppose the AC is initially cleared (contains all zeros).
  If Register B contains 0101 initially, then an arithmetic add, which we might denote by the symbol ADD B, an ADD B instruction will cause 1011 ( 0110 + 0101 ) to be stored in the AC .
Computer Organizati4o1n
Lecture 1

## Slide 39: 3. Accumulator (AC):
For Example:
  In this case , the sum of the numbers placed in Register B is Accumulated in the AC.
  Frequently in microprocessors all inputs and out -puts data must pass through the AC.
  The size of the Register is equal to the size
of a data word.

## Slide 40: 4. Program Counter ( PC):
The program counter contains the address in memory of the instruction being processed .
The set of instructions ( or program steps) is normally stored sequentially in memory.

## Slide 41: 4. Program Counter ( PC):
For Example:
  The following steps might be desired:
    Read a data word from the I/O device into the
Accumulator ( call this instruction L1 ).
    Add a number to the Accumulator( L2 ).

## Slide 42: 4. Program Counter ( PC):
For Example:
  Write the result into a certain memory location ( L3).
  The location of these instructions in memory in Fig 5.

## Slide 43: 4. Program Counter ( PC):
L4
L1
L2
L3
Figure 5. Location of instruction in memory

## Slide 44: 4. Program Counter ( PC):
For Example:
  In the normal step–by-step of instructions the computer accesses sequential locations in memory
  For this reason the Program Counter is normally incremented during execution of an instruction.

## Slide 45: 5. Stack:
The Stack is an array of Registers that allows words or addresses to be accessed from the top of this array on a last-in, first-out basis ( LIFO ).
A Stack is often termed an LIFO array or it may be referred to as a push down ( or push- pop) array.
Operation of a stack is shown in Fig 6.

## Slide 46: 5. Stack:
Figure 6. operation of a stack ( the storage & recall of a word)
Lecture 1 Computer Organizati4o9n
A3
A2
A1
A3
A2
A1
A4
A3
A2
A1
Push operation
Pop operation
Recall A4
Store A4

## Slide 47: 6. Stack Pointer:
47
Is used to hold the address of the top element of the stack.
Operation of the Stack Pointer .
Lecture 1
Computer Architecture

## Slide 48: 7. general-Purpose Register:
48
A number of Registers are provided in the CPU for temporary storage of data and addresses, in most Microprocessors .
The number of these Registers varies greatly from
computer to computer
Lecture 1
Computer Architecture

## Slide 49: 8. Instruction register ( IR ):
49
The IR contains the instruction being decoded and executed .
Input to the IR is typically from memory as the program steps are read sequentially.
Lecture 1
Computer Architecture

## Slide 50: 9. Status Register:
50
It consists of one or more Flip-Flops, often called flags, is used to provide indication of overflow from operations, presence of 0’s in the accumulator, sign of a number in the accumulator, and carry from the accumulator.
Lecture 1
Computer Architecture

## Slide 51: Levels of Representation
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Spec
Compiler
Assembler
Machine Interpretation
temp = v[k]; v[k] = v[k+1]; v[k+1] = temp;
lw $15, 0($2) lw $16, 4($2) sw $16, 0($2) sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
ALUOP[0:3] <= InstReg[9:11] & MASK

## Slide 52: Levels of Abstraction
Application
Libraries
Operating System
Programming Language
Assembler Language
Graphical Interface
Processor
IO System
Logic Design
Datapath and Control
Circuit Design
Semiconductors
Materials
Firmware
Circuits and devices
Fabrication
Digital Design
Computer Design
Application Programming
System Programming
Microprogramming
Instruction Set Architecture - “Machine Language”

## Slide 53: The Instruction Set: A Critical Interface
Instruction Set Design
  Machine Language
  Compiler View
  "Computer Architecture"
  "Instruction Set Architecture"
"Building Architect"
instruction set
software
hardware
Computer Architecture and Design
  Machine Implementation
  Logic Designer's View
  "Processor Architecture"
  "Computer Architecture "
"Construction Engineer"
Computer Architecture = Instruction Set Architecture + Machine Organization
This course

## Slide 54: Instruction Set Architecture
. . . the attributes of a [computing] system as seen by the programmer, i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation.
Amdahl, Blaaw, and Brooks, 1964
Data Types
  Encoding and representation
Memory Model
Program Visible Processor State
  General registers
  Program counter
  Processor status
Instruction Set
  Instructions and formats
  Addressing modes
  Data structures
System Model
  States
  Privilege
  Interrupts
  IO
External Interfaces
  IO
  Management
Architecture Reference Manual
Principles of Operation
Programming Guide
…

## Slide 55: Today, “Computers” are Connected Processors
Proc
Caches
Busses
Memory
I/O Devices:
Controllers
adapters
Disks
Displays
Keyboards
Networks
All have interfaces & organizations